## Slide 1
Optimal Control of Systems
Given a system: ; ; ; x(0) = x0
Find the control u(t) for t e [0,T] such that
Instantaneous (Stage) Cost
Terminal Cost
Can include constraints on control u and state x
  (along trajectory or at final time):
Final time T may or may not be free (we’ll first derive fixed T case)

## Slide 2: Solution approach
Add Lagrange multiplier (t) for dynamic constraint
  And additional multipliers for terminal constraints or state constraints
Form augmented cost functional:
where the Hamiltonian is:
Necessary condition for optimality: vanishes for any perturbation (variation) in x, u, or  about optimum:
x(t) = x*(t) + dx(t); u(t) = u*(t) + du(t); l(t) = l*(t) + dl (t);
Variations must satisfy path end conditions!
“variations”

## Slide 3: Pontryagin’s Maximum Principle
Optimal (x*,u*) satisfy:
Can be more general and include terminal constraints
Follows directly from:
Optimal control is solution to O.D.E.
0
0
0
0
Unbounded controls

## Slide 4: Interpretation of 
Two-point boundary value problem:  is solved backwards in time
 is the “co-state” (or “adjoint” variable)
Recall that H = L(x,u) + Tf(x,u)
If L=0, (t) is the sensitivity of the cost to a perturbation in state x(t)
  In the integral as
  Recall J = … +(0)x(0)

## Slide 5: Terminal Constraints
Assume q terminal constraints of the form: (x(T))=0
  Then
    (T) = (x(T))
  Where n is a set of undetermined Lagrange Multipliers
  Under some conditions, n is free, and therefore (T) is free as well
When the final time T is free (i.e., it is not predetermined), then the cost function J must be stationary with respect to perturbations T: T* + dT. In this case:
H(T) = 0

## Slide 6: Example: Bang-Bang Control
u
-1
H
+1
lT B>0
“minimum time control”
Since H is linear w.r.t. u, minimization occurs at boundary